## Slide 1
Neuromorphic Robotics for Drones
Roy Ben Hayun
LinkedIn: http://il.linkedin.com/in/roybenhayun
Email: roy.ben.hayun@climate-eyes.earth

## Slide 2: Agenda
Introduction
Articles
  Neuromorphic PID controller – 1DoF study
  Optic-Flow based landing
  Event-driven vision and motor-control
  Dynamic topology network
Practical work

## Slide 3: Drones in a nutshell
Notes: How it’s built
Reference drone

## Slide 4: Usages and challenges
Notes: Usages:
Agriculture, construction, HLS, defense, delivery, search and rescue

## Slide 5: Neuromorphic computing in a nutshell
Neuromorphic Algorithms
Neuromorphic Hardware
Notes: SNN
brain-inspired software models used in neuromorphic computing
asynchronous and event-based nature
HW:
Not Von Neuman. neuronal models realized in hardware, computed in real time, with co-location of memory and computing units.
Low power due to event-based asynchronous architecture
1+1
Lead to low power, low latency architectures.
orders of magnitude gains in power and performance.
additional key benefit of on-chip plasticity enabling continuous learning in real-time
GENERAL
using large artificial neural networks comes with the need of a large amount of processing power spike neural networks on the other hand
are a type of artificial nerves much closer to the biological nerns they accumulate input current and set out as spike whenever their internal variable the membrane potential reaches the threshold
specialized hardware has been developed to simulate such spike nearings with the goal of low latency and low power usage
while being able to scale to millions of neurons
many of you will already know about artificial neural networks the neurons model based on a very simplified version of the neurons in the biological brain. the artificial neuron summarizes the weighted inputs and outputs a value calculated by a time independent transfer function of the summarized inputs
artificial neurons have no mean of time and therefore no memory
spike neurons heavily rely on memory enzyme a spike neuron integrates the input current over time until a vulture threshold is reached at this time the neuron will send a spike through the connections called synapses to a postsynaptic nerve
the voltage potential of each neuron is calculated at each time step which uses a lot of power when

## Slide 6: Why neuromorphic computing for drone?
Energy constraints
Latency
Stochastic environments
Power \ Precision
Latency
Edge AI \ Learning
Notes: Robotics challenges
Motor control, perception, planning, decision making
constraints on latency, energy, and payload
Fit of NBE
precision and energy.
very importantly - learn as they move.
Similar to how biological neural networks allow perception, planning, control and learning with limited energy and limited local sensing only.
FAQ
Why not ANN
substantial computing power often with GPUs
large amount of prepared data for training
ANNs tend to grow

## Slide 7: Will autonomous drones replace a skilled human?
https://www.youtube.com/watch?v=PLMgMqMrQ98
Notes: if you look at the performance of autonomous drones today they are still far from human pilot performance in terms of speed versatility and robustness
The promise of Neuromorphic Computing to drones is therefore to create smart algorithms and learning systems that will expose cognitive capabilities in real time with improved energy consumption and latency, allowing to design robust and efficient autonomous flight systems for autonomous drones.

## Slide 8: Agenda
Introduction
Articles
  Neuromorphic PID controller – 1DoF study
  Optic-Flow based landing
  Event-driven vision and motor-control
  Dynamic topology network
Practical work

## Slide 9: Overview
Motivation: aim to unified neuronal architecture, start with motor control
Goal: design and performance improvements of the PID Controller
Improve a 1 DOF neuromorphic PID Controller
https://youtu.be/lnGQqz7MM8w
Notes: rotating between -20◦ to +20◦ on the Y axis, according to a given desired angle.
Motivation: aim toward integrated neuronal capabilities, starting from motor control. motor control will be tightly integrated into a unified neuronal architecture.
Goal: improvements before progressing further

## Slide 10: System overview
IMU node
ESC node
Control Setpoint node
Loihi node
Current setpoint
Current setpoint
Current setpoint
Motor command
Motors

## Slide 11: Baseline work: existing neuromorphic PID Controller
e(t)
subtracting control from sensory feedback
i(t)
adding current error with last integrated error
d(t)
subtracting delayed error from current error signal.
EM
IM
DM
P
I
D

## Slide 12: Baseline work: existing neuromorphic PID Controller
1) The sensor feedback (y) is subtracted from the setpoint (r) to obtain the error value (e)
index encodes input value One neuron each time
2) the error on one time step is subtracted from the error on the previous time step to obtain the derivative term.
integration module computes the integral of the error

## Slide 13: Improvement and redesign of the PID Controller
Issues:
  Sensors and host CPU delays
  Long time-step duration
  Number of time-steps
  Two nested PID controllers
Goals:
  Redesign I-path
  Simplify SNN
  Improve IO integration

## Slide 14: Improved SNN I-path (high SNN expertise)
3. c+ and c− are counter neurons
(High threshold, low leakage)
integrate positive and negative errors
4. ShiftDown and ShiftUp
shift active neuron in I population
Excite or inhibit I neurons
5. I-term output population
Place-Coding
1. Current error population
2. Red: Inhibitory connections
2. Black: Excitatory connections
2. Weights depend on index
Notes: Solves oscillation caused due to 63 neurons low-resolution in input neurons
When C fires it excites all neurons in I
Only 1 will be excited also by the I population and therefore activated
SNN expertise in a nutshell
e has weights depending on index, and usage of Excitory and Inhibitory
C have high threshold and low leakage
For Shift neurons to fire, also the respective I neuron must fire same time with C
Shift neurons excite or inhibit I neurons
Place coding vs Rate coding vs Temporal coding
  E.g., Place is easier for output command, Rate is better for summation
Shift up \ down, Accumulate

## Slide 15: Improvements ready for rigorous testing
Before:
  I-term saturation
  Two nested controllers
  IO delays
  20kHz frequency
  12 time-steps
  27ms time-step duration
  54 neuro-cores
After:
  Robust I term
  Single PID controller
  Improved IO
  1kHz frequency
  6 time-steps
  10ms time-step duration
  38 neuro-cores

## Slide 16: Results, Comparison and Conclusions
Slightly higher overshoot
Slightly faster rise time
Similar settling time
Goal achieved: drastic improvement of the neuromorphic PID Controller

## Slide 17: SNN output network
1. All 3 split to 2 pos\neg populations
2. Scaled and summed in population B
3. Output population U
4. Output signal converted to motor command
X86 maps the spikes’ source index to a value in the range [−1, 1]Nm.
Synaptic weights of respective PID gain
Excitory one-to-one connections
Inhibitory connections to all lower indices neurons
Neuron threshold
Values between
[−lim, lim].
Notes: SNN expertise
In output network, neurons connect to varying number of neurons
Linearly decreasing threshold
Bias current equal to middle neuron injected to all
Transition from Place Coding to Rate Coding

## Slide 18: Agenda
Introduction
Articles
  Neuromorphic PID controller – 1DoF study
  Optic-Flow based landing
  Event-driven vision and motor-control
  Dynamic topology network
Practical work

## Slide 19: Overview
Motivation: bridging the reality-gaps (sim to real world, real neuro-chip)
Goal: run SNN on Loihi integrated on real drone
reality gap between simulation and the real world
https://youtu.be/LGkjlG-OjaU
Notes: In previous work:
demonstrate learned neuromorphic control for a real-world problem through evolving SNNs for performing divergence based landings
reduce the spike rate of the SNN controller
In this work:
Motivation: bridging the other reality gaps which were not handled in the neuro-evolution work
Goal: land with the trained SNN, running on Loihi on drone

## Slide 20: Background: Optic Flow Divergence
Location of tracked point in previous frame
Location of tracked point in current frame
NOTE: not using neuro-chip yet
Notes: Reminder:

## Slide 21: Background: Neuro-evolution algorithm
Evolution starts with [4] randomly initialized population of [100] individuals
  Each individuals tested in same [4] varying landings
  Fitness of individual is evaluated
    by time to land, final height, final vertical velocity, total spike rate
  Selection carried out
  Weights and parameters are mutated every generation [total 400 generations]
At all time – “hall of fame” is kept
Hall of fame individuals are tested in 250 landings
Best performing individuals go for real-world tests

## Slide 22: Three layers SNN (20 | 10 | 5)
10 neurons
5 neurons
20 neurons
Position-Coding
decoding from spikes
to continuous Tsp
Red variables are the
evolved parameters.
Notes: W is the synapse value
Theta is the threshold value
a,t are decoding-related scale-parameters – may cause delays

## Slide 23: From evolving in simulation to real-world
Measure: oscillations, landing time, touch-down velocity, spike rate etc
Conclusion: bridged simulation to real-world
Best performing individuals
But, not using neuro-chip!
(Using TinySNN – a C implementation – on CortexA)

## Slide 24: Integration of Loihi with drone and CPU

## Slide 25: Integration of Loihi with drone and CPU

## Slide 26: From simulation to neuro-chip: Loihi LIF model
Gaps:
  Variances in neuron LIF models
  Loihi neurons update cycle
Adjustments:
  Mimic Loihi neurons, delay buffers

## Slide 27: From simulation to real-world: Loihi on real drone
Intermediate pre-flight testing: comparison with offline Loihi chip
Comparison with Loihi integrated on real drone
(Adjust) and record
Offline Loihi
Loihi on drone
Notes: Record: input (divergence error), output (thrust setpoint), spikes in hidden layer

## Slide 28: Results
https://youtu.be/LGkjlG-OjaU
Simulation and offline pre-flight
Real-world drone with Loihi
Notes: Using an evolutionary approach, closed the reality gap between simulated and on-chip SNNs
resulting controller consisting of only 35 neurons.
real-world landing tests from 4m, proved robust and consistent.

## Slide 29: Agenda
Introduction
Articles
  Neuromorphic PID controller – 1DoF study
  Optic-Flow based landing
  Event-driven vision and motor-control
  Dynamic topology network
Practical work

## Slide 30: Overview
Motivation: neuromorphic capabilities integrated for high speed
Goal: integrate neuromorphic event-based vision, motor-control, learning
Integration of event-vision and motor-control for high speed
https://youtu.be/EcZ_Nq6Z89U
Notes: In previous work:
In this work:
Motivation: need faster sensors, faster algorithms, faster processing. Unified neuromorphic architecture has a promise to fulfil.
Goal: integrate neuromorphic event-based vision, motor-control

## Slide 31: System overview

## Slide 32: Neuromorphic Sub-Systems Overview
Event based vision
Motor control
On-chip learning
Notes: visual line-tracking

## Slide 33: Event-Camera
Notes: HT
Points laying on the same line in the Cartesian space are mapped to intersecting sine curves in the Hough space (the -r space).
Therefore, for many points on the same line, the (; r) pair with the highest intersection density represents the correct line in Cartesian space.

## Slide 34: Hough-Transform to event-based
Notes: HT
Points laying on the same line in the Cartesian space are mapped to intersecting sine curves in the Hough space (the -r space).
Therefore, for many points on the same line, the (; r) pair with the highest intersection density represents the correct line in Cartesian space.

## Slide 35: Event Based Vision SNN
A: Event-stream down-sampled
B: represent events in
Cartesian Space
C: represent events in
Hough Space
D: connecting all neurons that correspond
to the same to a respective readout (“angle”) neuron
E: cleaning up activity
F: “memory” storing activity from
the previous time step.
for stationary scenarios

## Slide 36: Motor Control - PD Controller

## Slide 37: On-chip learning
4. when R neurons fire, synaptic weight changes according to learning rule
1. Place-Coding representation of err(t)
2. R neurons accumulate errors.
Fire only if reached threshold
Weights are proportional to error magnitude
6. Feedforward term
err(t)
Weights are negative or positive according to f
3. F neurons responsible for increasing and decreasing the feedforward term
5. B uses Multi-Shot Position-Coding by ordered thresholds
Notes: adaptive term in the controller that modifies the controller output in case the PD controller fails to remove the error (e.g., due to added load).
compensate for extended periods of large steady-state errors.
additive feed-forward layer that connects the input population to the output u
learning rule on Loihi can be composed by a combination of pre- and post-synaptic spikes, auxiliary variables representing recent activity, and a third factor, called the reinforcement channel.

## Slide 38: Comparison with CPU
Low-speed tracking
High-speed tracking - RMSE
Notes: High-speed: visual processing running 20-times faster on Loihi
Low-speed: network’s parameters tuned for high speed. So worse performance of the SNN.

## Slide 39: On-chip learning
Notes: additional weight of 125g attached to one side of the drone’s arm.

## Slide 40: Results
Integrated fast event-based vision and event-based control
Achieve very low latency fast processing at extremely low power
Explored on-chip learning with external disturbances
Pave the way to more neuromorphic applications
Notes: Other optimizations:
Efficient neuron allocation
More neurons in 1D allowing finer\wider values
AER integration
DMA instead of UART

## Slide 41: Agenda
Introduction
Articles
  Neuromorphic PID controller – 1DoF study
  Optic-Flow based landing
  Event-driven vision and motor-control
  Dynamic topology network
Practical work

## Slide 42: Deep Neuromorphic Controller with Dynamic Topology
Motivation: Need for multiple tasks at dynamic environments with disturbances, without pre-training
Goal: formulate flexible and stable learning approach for changing network topology
Disclaimer: article is “work in progress” stage
Neuronal networks that change their topology at runtime
Notes: In previous work:
In this work:
Motivation: Goal:

## Slide 43: Dynamically changing topology example
Increase of decrease the network capacity based on criteria (Bias, Variance) and inspired from several models
Notes: High Variance == Over Fitting => prune nodes
High Bias == Underfitting => Add nodes

## Slide 44
Reference signal
e(k-2)
e(k-1)
e(k)
u(t)
1. created with a single hidden layer and single node.

## Slide 45
2. high-bias condition is identified, new node inserted

## Slide 46
3. significant change in dynamics identified, layer expansion
Notes: Concept Drift Detection Method (mean gradient, confidence level) indicates on need
Copy last layer
New weights between prev and new (will be adjusted)
New weights copied

## Slide 47
4. high-bias condition is identified, new node inserted

## Slide 48
4. high-variance identified, node pruned

## Slide 49
A. High Bias condition
B. High Variance condition
C. Node contribution
A. Gradient mean bias
B. Saturated performance

## Slide 50: Compare fixed and dynamic capacity models
In Simulation, track a circle trajectory with slow and fast speed

## Slide 52: Compare fixed and dynamic capacity models

## Slide 53: Compare fixed and dynamic capacity models

## Slide 54: Compare fixed and dynamic capacity models

## Slide 55: Compare fixed and dynamic capacity models

## Slide 56: Agenda
Introduction
Articles
  Neuromorphic PID controller – 1DoF study
  Optic-Flow based landing
  Event-driven vision and motor-control
  Dynamic topology network
Practical work

## Slide 57: Practical work
Motivation: neuromorphic capabilities integrated to unified architecture
Goal: start from the most basic building block
PID controller with Nengo and AirSim
Notes: In previous work:
In this work:
Motivation: need faster sensors, faster algorithms, faster processing. Unified neuromorphic architecture has a promise to fulfil.
Goal: integrate neuromorphic event-based vision, motor-control

## Slide 58: Simulation environment

## Slide 59: Neuromorphic PID Controller

## Slide 60: Neuromorphic PID Controller

## Slide 61: Tuning the SNN
Number of Neurons
Radius
Integrator tau
Synapse

## Slide 62: CPU vs SNN – overall comparable

## Slide 63: 1. Same configuration, different number of neurons

## Slide 64: 2. Same PIG Gains, different radius, synapses

## Slide 65: 3. Integrator radius
Integrator radius=3
Integrator radius=1

## Slide 66: Observations
More parameters controlling e.g., gains, radius, synapses, neurons => impact on PID tuning with more parameters
Radius works as Clamping
Builtin Integrator slow response
Harder to debug
More complex then a CPU-PID which is pretty much straightforward (again, not expecting a win in this simplistic example)
Inaccuracy of outputs is reflected e.g., after settling

## Slide 67: Observations
Variability of behavior in SNN-PID resulting from the non-deterministic and imperfect accuracy of neurons output
Wider spectrum of variability due to the additional tunable parameters beyond PID Gains e.g., number of neurons, radius, synapses etc
Different behavior dynamics between deterministic rigid dynamic in imperative CPU-PID and softer with variability dynamics in neuromorphic SNN-PID

## Slide 68: Demo

## Slide 69
Neuromorphic Robotics for Drones
Roy Ben Hayun
LinkedIn: http://il.linkedin.com/in/roybenhayun
Email: roy.ben.hayun@climate-eyes.earth